## Slide 1
From activity counts to measured silicon watts
wattson power calibration · i.MX 95 · per-rail models driven by QEMU
Thesis under test: a functional emulator's activity counts, regressed against measured per-rail silicon power, can predict the power of applications the model has never seen.
RESULT: 6.4% mean error on total power, 50 real applications, predicted BLIND
Predictions were committed to git before a single power sample was taken on these applications. Coefficients came from an 11-point synthetic grid containing none of them.
Kyle Fox · IMX95LPD5EVK-19 + NXP BCU per-rail shunts · qemu-aarch64 TCG plugins · 2026-09-10

## Slide 2
Two questions
The second one is the one people ask for. The first one is the one that has to be true first.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
2
1
Can QEMU predict the ACTIVITY a workload generates on silicon?
YES for instruction activity — 1.7% mean error over 50 applications, 41 of 50 within 2%.
Memory bandwidth is over-reported by roughly 2x. Bounded, understood, and localised to streaming workloads.
2
Can that activity be turned into a POWER number?
YES — 6.4% mean error on total power, 14.8% worst, on 50 applications the model never saw.
And 3.6% on concurrent multi-application mixes. In both cases QEMU supplies the activity; the mW-per-unit-activity always comes from measured silicon.
Every number on this page is measured on silicon and predicted from an emulator that never ran on it.

## Slide 3
What we did
Eight steps, in order. Each one had to work before the next was meaningful.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
3
# | step | what came out
1 | Get the instrument | IMX95LPD5EVK-19 — the only i.MX 95 board with per-rail shunts. Flashed to match the FRDM's BSP first: the idle floor moves 29% between kernels.
2 | Measure the idle floor | n=5, spreads ≤1.7%. 1139.5 mW total; vdd_soc is 72% of it, vdd_arm only 13%.
3 | Ask what predicts core power | Instruction count — the activity vector's core term — explains R²=0.031. THREE PERCENT.
4 | Find what does | A 2-D grid varying ALU rate and bandwidth INDEPENDENTLY. Both together: R²=0.990.
5 | Add the missing term | 598 Mops/s on 2 cores = 656 mW; 599 on 1 core = 465 mW. Active cores matter on their own.
6 | Validate QEMU's counters | Same static binary under perf and under QEMU: instructions 0.1%, misses 0.01% in steady state.
7 | Freeze predictions for 50 apps | Committed to git BEFORE any power measurement of those apps.
8 | Measure and compare | 6.4% mean error on total power.

## Slide 4
Part 1 — Does QEMU see the work the silicon does?
Instruction activity: QEMU's count against the A55's own inst_retired counter, same binary, same input, 50 applications.
wattson activity · QEMU counts DERIVED from TCG plugins · silicon counts MEASURED via ARM PMU on i.MX95 (A55 core 0, pinned 1.8 GHz) · 2026-09-10
4
1.75% mean error, 0.65% median. QEMU counts the work.
23
of 50 within 0.5%
28
of 50 within 1%
41
of 50 within 2%
45
of 50 within 5%
5
of 50 above 5%
The ten applications that agree least well — the whole tail, nothing hidden:
application | QEMU G-insn | silicon G-insn | error
bb-cksum | 0.27 | 0.32 | -15.4%
bb-b64 | 0.73 | 0.83 | -12.6%
lz4-fast | 0.28 | 0.30 | -7.5%
parson | 1.90 | 2.00 | -5.2%
chase | 0.21 | 0.20 | +5.1%
application | QEMU G-insn | silicon G-insn | error
bb-md5 | 0.42 | 0.44 | -4.3%
chase-big | 0.32 | 0.33 | -3.6%
bb-awk | 2.59 | 2.67 | -2.9%
bb-sortn | 16.43 | 16.78 | -2.1%
mem | 0.54 | 0.55 | -2.0%
This is the activity factor a power model consumes. It is also, on its own, the thing you want when you are reading code flows and usage — how much work a workload does, where it does it, and how that changes when the code changes.

## Slide 5
Part 1 — Where QEMU does not see the same work
Memory bandwidth. QEMU's DRAM proxy against the A55's l3d_cache_refill counter.
wattson activity · QEMU counts DERIVED from TCG plugins · silicon counts MEASURED via ARM PMU on i.MX95 (A55 core 0, pinned 1.8 GHz) · 2026-09-10
5
QEMU over-reports DRAM bandwidth by roughly 2x — the one place it does not match the silicon.
application | QEMU GB/s | silicon GB/s | error | core-rail impact
mem-w | 4.66 | 2.62 | +78% | 124 mW
mem | 4.93 | 2.53 | +95% | 145 mW
mm-big | 1.49 | 0.60 | +149% | 54 mW
Those are the only 3 applications of 50 that exceed 0.5 GB/s.
The cause is write streaming: the A55 skips read-for-ownership on a full cache-line write, so the line is never fetched from DRAM. QEMU's cache model allocates it anyway and counts a transaction the silicon never issued. It is a known, single-mechanism gap — not noise — and it is the one piece of upstream work this campaign produced.
Why the power result survives it: 47 of 50 applications run below 0.5 GB/s, where the entire bandwidth term is worth under 27 mW of a ~1400 mW budget. The error is real, it is in the right place to be harmless for application workloads, and it is the first thing to fix before this is pointed at streaming or DMA-heavy code.

## Slide 6
Part 2 — The power models
Measured on silicon, driven by QEMU activity. Valid at the stated OPP — the frequency is part of the claim.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
6
vdd_arm = 243.8 + 0.1266·ALU Mops/s + 60.62·GB/s + 169.3·active_cores
vdd_soc = 851.0 + 0.0043·ALU Mops/s + 20.40·GB/s
DRAM = 45.7 + 160.06·√(GB/s) R² = 0.994
mW, at 1800 MHz. vdd_soc holds at 900 MHz unchanged (2.5% MAPE). vdd_arm needs its own per-OPP set.
rail | form | accuracy | note
vdd_soc | bandwidth only | 2.5–7% | transfers across OPPs unchanged
vdd_arm | alu + bandwidth + cores | 4–5% | per-OPP coefficient sets; halving the clock roughly halves this rail
DRAM group | saturating in bandwidth | R²=0.994 | intercept PINNED to the measured idle floor
⚠ The DRAM fit with the HIGHER R² is the more dangerous one: a quadratic scores 0.9984 but its negative BW² term predicts FALLING power above ~17 GB/s. The √ form costs 0.004 of R² and stays physical.

## Slide 7
Part 2 — The finding that changes the model
We expected instruction count to drive core power. It does not.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
7
instructions alone: R² = 0.031 mean error 48%, worst 149%
bandwidth alone: R² = 0.784 both + active cores: R² = 0.990, mean error 3.6%
An instructions-only model predicts 1197 mW where the board draws 481.
aspect | detail
the observation | a memory-stalling workload drew 760 mW on the core rail; a compute workload retiring MORE instructions drew 474 mW
why | a stalled core still burns clock trees, speculation, replayed loads, prefetchers and the L2/bus interface
confirmed twice | real Dhrystone vs real STREAM: vdd_arm ratio 1.02 — same core power, utterly different instruction mix
independent | Walker et al. (TCAD 2017) regressed PMCs against ODROID-XU3 per-cluster rails. Retired instruction count is NOT in their model either.
Consequence: an activity factor built on instruction count alone MIS-RANKS exactly the memory-bound workloads that dominate a real power budget.

## Slide 8
Part 2 — The blind test, 50 applications
Predictions committed to git before the board was touched. This is the headline result.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
8
Coefficients fitted on an 11-point synthetic alu/mem grid. None of these 50 applications appear in it.
application | pred mW | meas mW | err
mem-w | 1744 | 1795 | 3%
mem | 1771 | 1767 | 0%
sgm | 1375 | 1614 | 15%
lz4-fast | 1359 | 1565 | 13%
mm-big | 1449 | 1558 | 7%
lz4 | 1342 | 1529 | 12%
chase | 1304 | 1295 | 1%
chase-big | 1306 | 1314 | 1%
alu | 1342 | 1355 | 1%
rd-ray | 1289 | 1367 | 6%
prediction error | value
MAPE, total power | 6.4%
median | 6.5%
p90 | 10.2%
worst, any single app | 15%
bias (signed) | -6.4%
Every number above is a PREDICTION ERROR.
workload power range | mW
what the 50 apps actually draw | 1295 – 1795 mW
what the model predicted they draw | 1289 – 1771 mW
Stated in mW, not as a ratio: the model must reproduce the RANGE, not just the average. A model predicting every app near the mean would still score a good MAPE.
Predictions run 6.4% low on average — a systematic offset, not scatter, and therefore correctable if a future revision wants it.

## Slide 9
Part 2 — All fifty applications
Every prediction, every measurement. Nothing selected, nothing dropped.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
9
GREEN ≤ 8% error · AMBER 8–12% · RED > 12% — the 8% line is the published bar for a good per-rail model, and is this corpus's own p90 (8.3%).
app | pred | meas | err
mem-w | 1744 | 1795 | 3%
mem | 1771 | 1767 | 0%
sgm | 1375 | 1614 | 15%
lz4-fast | 1359 | 1565 | 13%
mm-big | 1449 | 1558 | 7%
lz4 | 1342 | 1529 | 12%
rd-life | 1425 | 1525 | 7%
qoi | 1397 | 1524 | 8%
cr-blowfish | 1374 | 1517 | 9%
mm | 1346 | 1515 | 11%
sgm-a55-1t | 1357 | 1512 | 10%
cr-b64 | 1377 | 1506 | 9%
bb-md5 | 1358 | 1484 | 8%
sort-big | 1384 | 1482 | 7%
bb-gunzip | 1342 | 1478 | 9%
cr-md5 | 1379 | 1478 | 7%
cr-rc4 | 1336 | 1477 | 10%
app | pred | meas | err
sha256-big | 1397 | 1476 | 5%
bb-b64 | 1335 | 1476 | 10%
sort | 1378 | 1473 | 6%
bb-sha512 | 1380 | 1470 | 6%
bzip2-fast | 1349 | 1469 | 8%
bb-wc | 1371 | 1467 | 6%
sha256 | 1398 | 1458 | 4%
lua | 1363 | 1457 | 6%
cr-aes | 1378 | 1445 | 5%
bzip2 | 1337 | 1444 | 7%
heatshrink | 1346 | 1440 | 6%
bb-sortn | 1345 | 1438 | 6%
bb-cksum | 1316 | 1437 | 8%
rd-plasma | 1331 | 1434 | 7%
sqlite-heavy | 1350 | 1434 | 6%
bb-gzip | 1335 | 1433 | 7%
sqlite | 1351 | 1432 | 6%
app | pred | meas | err
parson | 1339 | 1432 | 6%
bb-awk | 1336 | 1428 | 6%
bb-sed | 1343 | 1425 | 6%
bb-sha1 | 1383 | 1421 | 3%
cjson | 1339 | 1420 | 6%
pcg | 1349 | 1419 | 5%
rd-mandel | 1317 | 1418 | 7%
bb-grep | 1347 | 1406 | 4%
httpp | 1360 | 1391 | 2%
pacman | 1343 | 1386 | 3%
pacman-big | 1343 | 1382 | 3%
tommath | 1324 | 1372 | 4%
rd-ray | 1289 | 1367 | 6%
alu | 1342 | 1355 | 1%
chase-big | 1306 | 1314 | 1%
chase | 1304 | 1295 | 1%
36 of 50 within 8% · 11 between 8 and 12% · 3 above 12% — mW predicted vs mW measured, on silicon the model never trained on.

## Slide 10
Part 2 — A realistic edge workload, all six cores busy
Perception, inference, storage, networking, imaging, rendering, running at the same time. No silicon ACTIVITY counter feeds these predictions — the activity is QEMU's. The energy coefficients, as everywhere in this deck, were measured on silicon.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C · activity DERIVED from QEMU TCG; PMU column MEASURED on silicon · 2026-09-10
10
3.6% mean error, 5.8% worst, across two to six concurrent applications.
what it is | applications running concurrently | cores | pred mW | meas mW | err | err (PMU)
AI + vision | pacman + sgm stereo | 2 | 1605 | 1704 | 5.8% | 6.0%
AI + vision + DB + net | pacman + sgm + sqlite + httpp | 4 | 2123 | 2189 | 3.0% | 3.1%
full edge stack, every core | pacman + sgm + sqlite + httpp + qoi + ray | 6 | 2612 | 2561 | 2.0% | 0.7%
pacman = genetic-AI trainer · sgm = stereo-vision disparity on real imagery · sqlite = in-memory OLTP · httpp = HTTP parsing · qoi = image codec · ray = ray tracer
Controls — synthetic and benchmark mixes over the same core counts:
what it is | applications running concurrently | cores | pred mW | meas mW | err | err (PMU)
compute-bound control | 4 x sha256 | 4 | 2304 | 2163 | 6.5% | 6.5%
mixed benchmark control | sha256 + mem + lz4 + sqlite + lua + bzip2 | 6 | 3065 | 2878 | 6.5% | 1.4%
The last column re-runs each prediction using activity measured on silicon instead of QEMU, which separates the model from the emulator. They agree on the edge mixes — so the error there is the model's, not QEMU's. They diverge only on the streaming control (6.5% vs 1.4%), where QEMU's DRAM proxy over-reports bandwidth. Edge workloads run at 0.4–0.7 GB/s and are barely exposed to it.

## Slide 11
What this licenses, and what it does not
The trust statement, quantity by quantity.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
11
claim | verdict | basis
predict the INSTRUCTION activity of an unseen app | YES | 1.75% mean, 41 of 50 within 2%
predict DRAM BANDWIDTH | NO | over-reports ~2x; write streaming is not modelled
predict total power of an unseen app | YES | 6.4% mean, 14.8% worst, 50 held-out applications
predict vdd_soc | YES | 4.1% mean, 7.1% worst — the strongest single result
predict vdd_arm on its own | PARTLY | 10.8% median but 25.2% worst; use the SUM, not this rail alone
predict a concurrent multi-app mix | YES | 3.6% mean, 5.8% worst, 2–6 apps
predict streaming or DMA-heavy code | NO | the bandwidth gap lands directly on it
use these coefficients at another frequency | NO | 1800 MHz set; vdd_soc transfers, vdd_arm does not
use these coefficients on another SoC | NO | stall-power sign is microarchitecture-specific
emit watts from QEMU alone | NO | QEMU supplies ACTIVITY; energy coefficients come from silicon
The standing rule survives the campaign unchanged: QEMU measures activity, engineers convert activity to energy. A board that reads real watts is exactly when that discipline matters most.
Everything above is reproducible from the repo: frozen predictions in git before measurement, raw per-app pairs in RESULTS-50.csv, and every limit stated beside the number it qualifies.

## Slide 12
Where the number actually comes from
QEMU never emits a milliwatt. It is worth being precise about which half of the prediction it supplies.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
12
power = 243.8 + 0.1266 · ALU Mops/s + 60.62 · GB/s + 169.3 · cores
MEASURED on silicon rails
mW per unit of activity
DERIVED from QEMU
the activity itself
quantity | where it came from | status | basis
the activity a workload generates | QEMU | proven here | 1.75% vs the A55's own PMU, 50 applications
mW per unit of activity | measured silicon rails | stood in for the engineers | 11-point calibration grid on a real board
mW per unit of activity, BEFORE silicon exists | gate-level power estimation | NOT tested here | this is the engineers' half, and it is the open link
In a real program that middle row is a power-estimation spreadsheet. Here we stood in for it by having the actual silicon. That is what makes this evidence rather than a proposal — with the energy side known-good, any error left over belongs to the activity side, which is the half under test. It is also why this does not replace the engineers: before tapeout there is no rail to measure, and the coefficients come from their estimates instead.
What this campaign de-risks is the QEMU half — so that when gate-power estimates arrive, the activity being fed into them is already known to be right.

## Slide 13
What this actually replaces
A power estimate is two numbers multiplied together. Only one of them has ever had a way to get better.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
13
gate power per toggle
the engineers' power-estimation spreadsheet
refines over time
Wide error bars early, and everyone knows it — but it REFINES as the design matures. Synthesis, then place-and-route, then silicon.
activity factor
a flat assumption: 1%, 2%, 3%, 5%, 10%
never refines
Does not refine. Nothing connects a toggle rate to a workload, so there is no mechanism by which the guess improves.
How do you correlate a 3% toggling assumption to a real use case? You cannot — there has been no instrument for it.
That is the gap this closes:
name an application
get its activity factor, per workload, with a stated error against silicon
change the code
see the activity factor move, and by how much
compare two use cases
on the same measured basis, not two different guesses
The spreadsheet keeps its job. It just stops being multiplied by a number nobody can trace to anything.

## Slide 14
What this actually means
The result is not the point. What it licenses us to do next is the point.
wattson power · rails MEASURED on IMX95LPD5EVK-19 (NXP BCU) · A55 die 40–41 °C under load · activity DERIVED from QEMU TCG · 2026-09-10
14
1
Predicting power on working silicon is not, by itself, worth much.
If the part exists, you can put a meter on it. Everything in this deck was validated against a board we already had — that is what makes it evidence, not what makes it useful.
2
So the value has to be collected BEFORE there is silicon.
Which sets a hard prerequisite on the program: a settled architecture and memory map, early, well ahead of tapeout — enough to stand up a QEMU model and boot a full Linux BSP on it. That is the gate. Not the power work; the model underneath it.
3
Once that exists, this campaign says both halves work.
QEMU predicts the activity factors — usable on their own for reading code flows, usage and where the work lands. And fed to a power model, those activity factors produced power estimates that held to single digits against real rails. The half still to prove is the model itself: here its coefficients were measured on silicon, and pre-tapeout they must come from gate-level estimation instead. That is the engineers' half, and it is the remaining risk.
The division of labour: QEMU supplies the activity. The power model supplies the energy. Neither one is asked to do the other's job.